## Slide 1: An event-triggered programmable prefetcher for irregular Workloads
Sam Ainsworth and Timothy M. Jones
Presenters: Leul Belayneh and Nicholas Wendt
Presentation for EECS 583

## Slide 2: Irregular Workloads are Everywhere

## Slide 3: Common Memory Accesses: Sequential
A
4
1
10
6
9
A[ i ]
Simple next-line prefetchers

## Slide 4: Common Memory Accesses: Indirect
A
4
1
10
6
9
B[ A[ i ] ]
B
Sequential
Irregular
Software prefetching

## Slide 5: Common Memory Accesses: List
A -­> next
B
Irregular
Event-based prefetching

## Slide 6: Pseudocode HashJoin
    // HashJoin algorithm
    // data structures initialization
    for(x = 0; x < in.size; x++){
    Hash h = hash(x);
    Bucket b = htab[h];
    ListElement l = b.listStart;
    while(l != NULL){
    if(l->key == k){ out.size++;}
    l = l->next;
    }
    }
Mem Indirect
List
List

## Slide 7: The problem: inefficient computation
Irregular workload execution in general purpose processors are characterized by:
  - Irregular memory accesses: difficult to capture using caches
  - Excess cache line size for small data (~8 bytes): waste of memory bandwidth
  - Low computational intensity: simple computations for each data

## Slide 8: Prior solutions
Fetcher Units*
  domain specific architecture
*Sqrl: Hardware accelerator for collecting software data structures. PACT, 2014
† Compiler-directed content-aware prefetching for dynamic data structures. PACT, 2003
‡ Design and evaluation of compiler algorithms for pre-execution. ASPLOS, 2002
Configurable Prefetchers†
  exposed at the architectural level
  target specific traversals
Helper Threads ‡
  uses separate CPU threads
  no extra hardware required
  - leads to heavy stalling to prefetch based on prefetches
  + higher performance
  memory-centric optimization
non overlapping memory accesses

## Slide 9: Key Idea – Memory-Level Parallelism
Observation: parallelizing loads via prefetching
Triggering a new prefetch by reacting to old prefetches and loads
How can we parallelise memory accesses instead of computation?

## Slide 10: Execution Flow: Events
Observe Load to A[n]
Prefetch A[n+N]
Prefetch B[A[n+N] ]
Prefetch C[B[A[n+N] ] ]
Original Code:
Events

## Slide 11: Architecture

## Slide 12: Architecture: Address Filter
Addr Filter

## Slide 13: Architecture: Scheduler
Scheduler

## Slide 14: Architecture: Prefetch Units

## Slide 15: Application Support
Requires event functions and an address table

## Slide 16: Application Support
Requires event functions and an address table

## Slide 17: Application Support
Requires event functions and an address table
Address Table:
2 1 0

## Slide 18: Compiler Assistance
Prefetcher can be integrated manually

## Slide 19: Compiler Assistance
Prefetcher can be integrated manually
Automated integration through two passes:
  Software prefetch conversion
  Loop pragmas

## Slide 20: Software Prefetch Example Program
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec

## Slide 21: Software Prefetch Example Program
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19

## Slide 22: Software Prefetch Example Program
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)

## Slide 23: Software Prefetch Example Program
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
19: return acc

## Slide 24: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8

## Slide 25: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
Prefetch is root of dependency graph

## Slide 26: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
Loop-invariant, stop
(constant)
C

## Slide 27: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
C
v5

## Slide 28: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
Loop-variant load, stop
(will be prefetched)
v5
C
v4

## Slide 29: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
// on_B_prefetch()
1: lshift offset, bVal, #3
2: prefetch fetch
Will run when B’s prefetch completes

## Slide 30: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
// on_B_prefetch()
1: get_data bVal
2: lshift offset, bVal, #3
3: prefetch fetch
Index | Base | End | Load Ptr | PF Ptr
1 | B | B+sizeb | 0 | &on_B_prefetch
Address Table
Triggering event’s data placed in a local register when scheduled

## Slide 31: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
// on_B_prefetch()
1: get_data bVal
2: get_base base, #2
3: lshift offset, bVal, #3
4: add fetch, base, offset
5: prefetch fetch
Index | Base | End | Load Ptr | PF Ptr
1 | B | B+sizeb | 0 | &on_B_prefetch
2 | C | C+sizec | 0 | 0
Address Table

## Slide 32: Software Prefetch Conversion
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ...
16: add v6, v0, #1
17: cmp v6, v0, #1
18: bne 8
// on_B_prefetch()
1: get_data bVal
2: get_base base, #2
3: lshift offset, bVal, #3
4: add fetch, base, offset
5: prefetch fetch
Process repeats for
B’s load… then A’s load…
Index | Base | End | Load Ptr | PF Ptr
1 | B | B+sizeb | 0 | &on_B_prefetch
2 | C | C+sizec | 0 | 0
Address Table

## Slide 33: Software Prefetch Conversion
Index | Base | End | Load Ptr | PF Ptr
0 | A | A+sizea | &on_A_load | &on_A_prefetch
1 | B | B+sizeb | 0 | &on_B_prefetch
2 | C | C+sizec | 0 | 0
Address Table

## Slide 34: Software Prefetch Conversion
Address Table
1: alloc A, sizea
2: alloc B, sizeb
3: alloc C, sizec
4: mov acc, #0
5: mov x, #0
6: cmp x, N
7: beq 19
// config_addr_tbl 0
// config_addr_tbl 1
// config_addr_tbl 2
8: phi v0, x, v6
9: add v1, v0, #128
10: load v2, v1(A)
11: lshift v3, v2, #3
12: load v4, v3(B)
13: lshift v5, v4, #3
14: prefetch v5(C)
15: ... // Load value, update acc
...
Software prefetch code is now unneeded, remove it
Load address table into address filter unit
Index | Base | End | Load Ptr | PF Ptr
0 | A | A+sizea | &on_A_load | &on_A_prefetch
1 | B | B+sizeb | 0 | &on_B_prefetch
2 | C | C+sizec | 0 | 0

## Slide 35: Loop Pragmas
Label loops with a pragma directive
Runs SPC-like pass on each load
More convenient for the programmer

## Slide 36: OS Support
OS only sees prefetcher’s context switching state
  Global PPU registers (loop-invariant values)
  Address table
  (All other state is discarded)

## Slide 37: OS Support
OS only sees prefetcher’s context switching state
  Global PPU registers (loop-invariant values)
  Address table
  (All other state is discarded)
PPU faults terminate their execution

## Slide 38: Evaluation Results: Speedup
Notes: Simulated OoO ARMv8 core in gem5 (running Linux)
Compared programmable prefetcher performance to:
  No prefetching (baseline)
  Stride prefetcher
  Markov global history buffer prefetcher
    2,048 entries
    67,108,864 entries
Used several memory-bound benchmarks
Note manual > spc > pragma
-All but G500: >~80% L1 prefetches utilized before eviction
-Speedup as L1 cache hit rates have increased (~2x increase)

## Slide 39: Analysis: Blocking Intermediate Loads

## Slide 40: Discussion
Presented a programmable, event-driven prefetcher
Provided compiler techniques to automate utilization
Demonstrated average speedups of 3x in memory-bound benchmarks
Small hardware footprint, ~3% area overhead on a Cortex A57
Must be targeted during software development to be useful
Compiler passes could be improved to close the gap with manual
Large amount of hidden state may hinder tuning

## Slide 41: Q/A
Thank you!

## Slide 42: Backup Slides
42

## Slide 43: Evaluation: L1 Evictions

## Slide 44: Evaluation: L1 Hit Rate

## Slide 45: Analysis: PPU Frequency

## Slide 46: Analysis: PPU Count

## Slide 47: Analysis: PPU Utilization