Objectives

- Explore general robot concepts including behaviors.

- Examine programming conventions using motor blocks, sensor blocks, sensor reset blocks, and looping structures.

- Develop computer programs for straight lines and circles/curves.

General

- What is a robot?  Go over general concepts of robots.

- They do only what we tell them to do and exactly what we tell them to do.  Therefore, if there is a problem, is it the robot or the programmer?

Procedure – Day One

  - Forward, both motors

    - Distance vs. time

    - Using motor blocks

  - Stop

- Both motors

- Why?

  - Measuring distance

- Always use the same point to line up and measure.

- Why?

  - Rotation sensor

- Built in

- Circle concepts – 360 degrees

- How far for 1 rotation, 2 rotations, etc.

- Traced circle vs. wheel diameter

  - Behavior concepts

- Simple behavior vs. complex behaviors (made up of 2 or more simple behaviors)

- Reset rotation sensors between behaviors

- 1 program block to reset rotation sensor

  - Fill in Chart 1

- Distance Traveled in Inches

- Instructor approval required on Rotation 1/360 degrees only.

- Check program for correctness before allowing to proceed.

Procedure – Day Two

  - Fill in Chart 2

- Number of Degrees required to go Particular Distance

- Instructor approval required on 6 inches only.

- Check program for correctness before allowing to proceed.

  - Stop, go over results.

- Students should have determined that it takes roughly 300 degrees to go 6 inches.

  - Task 1

- Make robot go forward 1 foot.

- Instructor approval required to proceed.

  - Task 2

- Make robot go forward 1 foot, backward 1 foot.

- Instructor approval required to proceed.

Procedure – Day Three

  - Turns

- Review terminology of turns

- Full right/Full left (90 degrees)

- Turn around/Face backward (180 degrees)

- Turn completely around (360 degrees)

- Swing turn only

  - Chart 3

- Number of degrees required to make a particular turn.

- Instructor approval required for quarter turn only.

- Check program for correctness before allowing to proceed.

Procedure – Day Four

  - Task 3

- Make robot go forward 1 foot, turn to face to the right of the current position, then go forward 1 foot.

- Instructor approval required to proceed.

  - Task 4

- Make robot go forward 1 foot, turn to face to the left of the current position, then go forward 1 foot.

- Instructor approval required to proceed.

  - Looping structures

- Determine nature of loop, i.e. infinite, number of times to repeat, period of time to run, etc.

Procedure – Day Five

  - Task 5

- Make robot go forward 1 foot, then backward 1 foot.  Repeat 4 times.

- Program must use a loop.

- Robot will have trouble with swivel wheel.

  - Task 6

- Make robot go in a square that is 12 inches on each side.

- Program must use a loop

  - Challenge

- Bonus grade

- Since this is a challenge, I can’t help.

- Hint:  We’ve talked about behaviors.  In order to correctly program this behavior, you must break the figure 8 down into its component behaviors which should be a series of straight lines and curves.  A loop will not work.

Assessment

- Chart 1

- Chart 2

- Chart 3

- Task Charts