## Slide 1: Data Center TCP (DCTCP)
Mohammad Alizadeh, Albert Greenberg, David A. Maltz, Jitendra Padhye Parveen Patel, Balaji Prabhakar, Sudipta Sengupta, Murari Sridharan
Presented and Adapted by Yikai Lin

## Slide 2: Outline
1. Problem Statement
2. Design Goals
3. DCTCP Algorithm
4. Analysis
5. Evaluation
6. Conclusions
7. Q&A

## Slide 3: Data Center Packet Transport
Cloud computing service provider
  Amazon, Microsoft, Google
Transport inside the DC
  TCP rules (99.9% of traffic)
How’s TCP doing?

## Slide 4: TCP in the Data Center
We’ll see TCP does not meet demands of apps.
  Incast
    Suffers from bursty packet drops
  Builds up large queues:
    Adds significant latency.
    Wastes precious buffers, esp. bad with shallow-buffered switches.
Operators work around TCP problems.
  Ad-hoc, inefficient, often expensive solutions
“Our” solution: Data Center TCP
Notes: Carefully control the amount of data each worker sends;
Add jitter to the data communication to avoid synchronization

## Slide 5: Case Study: Microsoft Bing
Measurements from 6000 server production cluster
Instrumentation passively collects logs
  Application-level
  Socket-level
  Selected packet-level
More than 150TB of compressed data over a month

## Slide 6: Workloads
Partition/Aggregate
(Query)
Short messages [50KB-1MB]
(Coordination, Control state)
Large flows [1MB-50MB]
(Data update)
Delay-sensitive
Delay-sensitive
Throughput-sensitive

## Slide 7
TLA
MLA
MLA
Worker Nodes
………
“Everything you can imagine is real.”
“Bad artists copy.
Good artists steal.”
“It is your work in life that is the ultimate seduction.“
“The chief enemy of creativity is good sense.“
“Inspiration does exist,
but it must find you working.”
“I'd like to live as a poor man
with lots of money.“
“Art is a lie that makes us
realize the truth.
“Computers are useless.
They can only give you answers.”
Picasso
Time is money
  Strict deadlines (SLAs)
Missed deadline
  Lower quality result
Deadline = 250ms
Deadline = 50ms
Deadline = 10ms
EECS 582 – W16

## Slide 8: Impairments
Incast
Queue Buildup
Buffer Pressure

## Slide 9: Incast
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
Synchronized mice collide.
  Caused by Partition/Aggregate.

## Slide 10: Queue Buildup
Sender 1
Sender 2
Receiver
Measurements in Bing cluster
  For 90% packets: RTT < 1ms
  For 10% packets: 1ms < RTT < 15ms

## Slide 11: Data Center Transport Requirements
High Burst Tolerance
  Incast due to Partition/Aggregate is common.
Low Latency
  Short flows, queries
3. High Throughput
  Large file transfers

## Slide 12: Balance Between Requirements
High Burst Tolerance
High Throughput
Low Latency
DCTCP
Deep Buffers:
Queuing Delays
Increase Latency
Shallow Buffers:
Bad for Bursts &
Throughput
Reduced RTOmin (SIGCOMM ‘09)
Doesn’t Help Latency
AQM – RED:
Avg Queue Not Fast
Enough for Incast
Objective:
Low Queue Occupancy & High Throughput

## Slide 13: Review: The TCP/ECN Control Loop
Sender 1
Sender 2
Receiver
ECN Mark (1 bit)
ECN = Explicit Congestion Notification

## Slide 14: Two Key Ideas
React in proportion to the extent of congestion, not its presence.
  Reduces variance in sending rates, lowering queuing requirements.
Mark based on instantaneous queue length.
  Fast feedback to better deal with bursts.
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%

## Slide 15: Data Center TCP Algorithm
Switch side:
  Mark packets when Queue Length > K.
  Sender side:
  Maintain running average of fraction of packets marked (α).
  In each RTT:
Adaptive window decreases:
  Note: decrease factor between 1 and 2.
B
K
Mark
Don’t
Mark
Notes: SRTT = (1-alpha)*SRTT+alpha*R’

## Slide 16: DCTCP in Action
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows, K = 30KB
(Kbytes)

## Slide 17: Why it Works
High Burst Tolerance
  Large buffer headroom → bursts fit.
  Aggressive marking → sources react before packets are dropped.
Low Latency
  Small buffer occupancies → low queuing delay.
3. High Throughput
  ECN averaging → smooth rate adjustments, cwind low variance.

## Slide 18: Analysis
Time
(W*+1)(1-α/2)
W*
Window Size
W*+1

## Slide 19: Analysis
Packets sent in this
RTT are marked.
Time
(W*+1)(1-α/2)
W*
Window Size
W*+1

## Slide 20: Analysis
How low can DCTCP maintain queues without loss of throughput?
How do we set the DCTCP parameters?
Need to quantify queue size oscillations (Stability).
85% Less Buffer than TCP
bandwidth-delay product

## Slide 21: Evaluation
Implemented in Windows stack.
Real hardware, 1Gbps and 10Gbps experiments
  90 server testbed
  Broadcom Triumph 48 1G ports – 4MB shared memory
  Cisco Cat4948 48 1G ports – 16MB shared memory
  Broadcom Scorpion 24 10G ports – 4MB shared memory
Numerous benchmarks
  – Throughput and Queue Length
  – Multi-hop
  – Queue Buildup
  – Buffer Pressure
– Fairness and Convergence
– Incast
– Static vs Dynamic Buffer Mgmt

## Slide 22: Evaluation
Background Flows
Query Flows

## Slide 23: Evaluation
Background Flows
Query Flows
Low latency for short flows.

## Slide 24: Evaluation
Background Flows
Query Flows
Low latency for short flows.
High throughput for long flows.

## Slide 25: Evaluation
Background Flows
Query Flows
Low latency for short flows.
High throughput for long flows.
High burst tolerance for query flows.

## Slide 26: Conclusions
DCTCP satisfies all our requirements for Data Center packet transport.
  Handles bursts well
  Keeps queuing delays low
  Achieves high throughput
Features:
  Very simple change to TCP and a single switch parameter K.
  Based on ECN mechanisms already available in commodity switch.

## Slide 27: Discussions
1. Will DCTCP perform worse in the internet?
2. How about SDN using fine-grained TE? OpenTCP?
3. Not compatible with SACK, which reduces the # of ACKs
4. Convergence really doesn’t matter?
5. RTT-fairness (favors small RTT flows)?
See “Analysis of DCTCP: Stability, Convergence, and Fairness”

## Slide 28: Q&A