## Slide 1: Delegated Persist Ordering
Aasheesh Kolli
Jeff Rosen
Stephan Diestelhorst
Ali Saidi
Steven Pelley
Sihang Liu
Peter M. Chen
Thomas F. Wenisch
MICRO 2016 - Taipei

## Slide 2: Promise of Persistent Memory (PM)
Non-volatility
Performance*
Byte-addressable, load-store interface to storage
Density

## Slide 3: Recoverable data structures in PM
Correct recovery relies on ordering writes to PM
prepareUndoLog (P)
mutateData (M)
commitTx (C)
Recoverable
Need primitives to express desired write order to PM

## Slide 4: Memory persistency models
Programmers can express write order to PM
Hardware enforces write order
Similar to memory consistency models
[Condit ‘09] [Pelley ‘14] [Intel ‘14] [Joshi ‘15] …

## Slide 5: Contributions
Implications of Synchronous Ordering [Intel ‘14]
  Semantics and performance
  7.2x slowdown over volatile execution
Delegated Persist Ordering
  Implementation strategy for persistency models
  3.5x speedup over Synchronous Ordering

## Slide 6: Outline
Background
Synchronous Ordering (SO)
SO drawbacks
Delegated Persist Ordering (DPO)
Evaluation

## Slide 7: Persistent memory system
Core-1
Core-2
Core-3
Core-4
L1 $
L1 $
L1 $
L1 $
LLC
DRAM
Persistent Memory (PM)
Recovery
Notes: A future persistent system would be multi-core, with a fairly traditional cache hierarchy, and with both DRAM and Persistent memory ion the memory bus.
We expect the address space to be partitioned into a volatile region, mapped to DRAM, and a persistent region, mapped to persistent memory.
In the event of failure, all the contents of the cores, caches and DRAM are lost, however the contents of the persistent memory are retained.
Upon restart, Recovery may inspect the contents of the persistent memory, to restore the system to a consistent state.

## Slide 8: Terminology
Persist
  Act of making a store durable in PM
Persist memory order (PMO)
  Memory events ordered by persistency model
  Governs the order in which stores persist
Notes: Memory events.
We define a persist to be the act of making a store durable in Persistent memory
Volatile Memory Order or VMO, order of memory events as desribed by the consistency model of the system.
I.E VMO governs the order in which loads and stores become visible to the other cores in the system.
In this study, we use TSO as the underlying consistency model.
The persist memory order of PMO, is the order of memory events as required by the perisstency model of the system.
This governs the order in which stores becomes durable in NVM.
While ordering stores is required for recovery correctness, reducing the ordering dependencies is essential for performance.
In this talk, I present results for only one persistency model,called epoch persistency, more detailed analysis with different persistency models can be found in the main paper.
----- Meeting Notes (3/29/16 17:24) -----
no as per
----- Meeting Notes (3/31/16 14:57) -----
constraints, why is fewer better

## Slide 9: Persistency model
Core-1
Core-2
L1 $
L1 $
LLC
PM
/* Init: a = 0, b=0
a,b are persistent */
Core-1 Core-2
St a = x
while (a==0){}
St b = y
Constraint: St a < St b
a
b
Consistency
Persistency
Writeback caching
Mem Ctrl reordering
Persistency models must minimize
additional performance overheads
Notes: In this slide, I want to differentiate consistency and persistency models.
On the left we have a simple piece of code, we initially have variables a and b set to zero. Both are backed to persistent memory..
Core -1 sets a to one, core-2 spins until a is set to one, followed by setting b to one.
So, we require that the stoer to a happens before store to b.
The responsibility of ensuring that the stores to a and B becomes visible to all the cores in the desired order is the responsibility of the consistency model.
However, if this ordering is required for recovery coorectness, we must ensure that a nd b also persist in order.
The responsibility of the persistency model is ensureing that a and b navigate the cache hierarchy and persist in order.
This impliest that typical perf enhancing techniques such as writeback caching and mem ctrl reordering, are not effective. So, ordering constrains, result in poor performance. The rest of this talk is about trying to gain the lost performance, without giving up on ordering guarantees.
----- Meeting Notes (3/29/16 17:24) -----
a and b are in pm, use notation, sta and stb, optimizations may not be correct also

## Slide 10: Epoch persistency [Condit ‘09, Pelley ‘14, Joshi ‘15]
FENCEs break thread execution into epochs
Persists across epochs are ordered
  No ordering within epoch
prepareUndoLog (P)
mutateData (M)
FENCE
PMO
P1
…
…
P2
Pn
M1
M2
Mn
Epoch-1
Epoch-2
However, many ways to skin a cat …

## Slide 11: Synchronous Ordering (SO)
Based on x86 ISA changes for PM
CLWB <Addr>
  Writes back cache block to Memory Controller (MC)
PCOMMIT
  Persists all accepted stores at MC
Cores
Caches
Mem Ctrl
PM
1. CLWB
2. PCOMMIT

## Slide 12: Ordering via stalling
Objective: persist A and B in order
St A = x
CLWB <A>
fence
PCOMMIT
fence
St B = y
Core
Caches
b
a
a
b
4
3 – completion ACK
Stalled
a
2
1
Ordering via stalling  frequent processor stalls

## Slide 13: Further drawbacks
Places the PCOMMIT on critical path
  Negates scheduling optimizations at the MC
  Has to respect all accepted stores at the MC
Explicit CLWB annotations from user
  Challenge for multi-party software dev
  Affects cache coherence permissions
7.2x slowdown for PCM main memories

## Slide 14: Ideal ordering
Objective: persist A and B in order
St A = x
fence
St B = y
Core
Caches
b
a
a
1
b
b
a
>
2
3
Buffered persistency [Condit ‘09] [Pelley ‘14] [Joshi ‘15]
Ordering without stalling

## Slide 15: Delegated Persist Ordering (DPO)
Goals
  Reduce processor stalls
  More scheduling freedom for MC
Key ideas
  Buffer persists & ordering info alongside cache hierarchy
  Decouple persistence from core execution
Challenge
  Accurately track persist order across cores

## Slide 16: Proposed architecture
Persist buffer at L1-D $
  Houses persist for each store to PM
  Retired fences
Dependency tracking
  Via coherence traffic
Persists drain to MC
  Decoupled from WBs
Core-1
Core-2
Core-3
Core-4
L1 $
L1 $
L1 $
L1 $
LLC
PM
MC

## Slide 17: DPO in action
/* Init: a = b = 0; a,b are persistent */
Core-1 Core-2
St a = x
while (a==0){}
fence
St b = y
Constraint: St a <p St b

## Slide 18: DPO in action
a | 1
St b = y
Core-1
LLC
PM
MC
St a = x
a
a
b
1
-
Ld a
a |
a |
a | 1
1
fence
fence
2
-
3
a
Core-2
ID
Deps
Blk
ID
Deps
Blk
b
/* Init: a = b = 0; a,b are persistent */
Core-1 Core-2
St a = x
while (a==0){}
fence
St b = y
Constraint: St a <p St b

## Slide 19: DPO highlights
Decouples persistence from core execution
Better scheduling at the MC
Fewer stalls at the core

## Slide 20: Experimental setup
gem5 simulator – details in paper
Workloads: write intensive micro-benchmarks
  Concurrent queue: insert/delete entries
  Array swaps: random swaps of array elements
  TATP: update location transaction from TATP
  RB-Tree: insert/delete entries
  TPCC: new order transaction from TPCC
PM configs
  PCM
  DRAM
  PWQ  assuming a persistent write queue at the MC

## Slide 21: Performance
Chart: 
| Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | PCM |  | DRAM |  | PWQ
SO | 5.7143 | 34.7917 | 15.7006 | 1.3382 | 4.9969 | 7.3099 | 2.9667 | 6.2771 | 3.9218 | 1.1745 | 3.019 | 3.0384 | 2.1587 | 1.8631 | 1.7232 | 1.1204 | 1.2921 | 1.5859
DPO | 1.746 | 4.5536 | 2.9322 | 1.0224 | 1.6249 | 2.0778 | 1.35 | 1.3193 | 1.067 | 1.0118 | 1.2896 | 1.1992 | 1.3016 | 1.3631 | 1.0791 | 1.012 | 1.3497 | 1.212
35
16
* Execution times normalized to volatile execution
Better
Execution times down with lower memory latencies
Normalized execution times

## Slide 22: Performance
Chart: 
| Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | PCM |  | DRAM |  | PWQ
SO | 5.7143 | 34.7917 | 15.7006 | 1.3382 | 4.9969 | 7.3099 | 2.9667 | 6.2771 | 3.9218 | 1.1745 | 3.019 | 3.0384 | 2.1587 | 1.8631 | 1.7232 | 1.1204 | 1.2921 | 1.5859
DPO | 1.746 | 4.5536 | 2.9322 | 1.0224 | 1.6249 | 2.0778 | 1.35 | 1.3193 | 1.067 | 1.0118 | 1.2896 | 1.1992 | 1.3016 | 1.3631 | 1.0791 | 1.012 | 1.3497 | 1.212
35
16
* Execution times normalized to volatile execution
Better
Normalized execution times
DPO consistently out performs SO for all mem configs
3.5x
2.5x
1.3x

## Slide 23: Recent developments
Cores
Caches
Mem Ctrl
PM
Persistent
domain
4 weeks ago 
Require persistent write queue (at MC)

## Slide 24: Performance
Chart: 
| Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | PCM |  | DRAM |  | PWQ
SO | 5.7143 | 34.7917 | 15.7006 | 1.3382 | 4.9969 | 7.3099 | 2.9667 | 6.2771 | 3.9218 | 1.1745 | 3.019 | 3.0384 | 2.1587 | 1.8631 | 1.7232 | 1.1204 | 1.2921 | 1.5859
DPO | 1.746 | 4.5536 | 2.9322 | 1.0224 | 1.6249 | 2.0778 | 1.35 | 1.3193 | 1.067 | 1.0118 | 1.2896 | 1.1992 | 1.3016 | 1.3631 | 1.0791 | 1.012 | 1.3497 | 1.212
35
16
* Execution times normalized to volatile execution
Better
Normalized execution times
1.3x

## Slide 25: Conclusions
Persistency model semantics affect performance
SO couples ordering with completion of persists
  Often unnecessary
DPO decouples persistence from core execution
DPO significantly outperforms SO

## Slide 26: Questions?

## Slide 27: Thank you!

## Slide 28: Backup

## Slide 29: DPO in action
Core-1 Core-2
St a = x
while (a==x){}
fence
St b = y
ID | Deps | Addr & Data
PBE:

## Slide 30: DPO in action
St b = y
Core-1
Core-2
LLC
PM
MC
St a = x
a
a
b
ID: 1
-
ID | Deps | Addr & Data
PBE:
Ld a
a |
a |
a | 1
a | 1
1
fence
fence
ID: 2
b
-
ID: 3
a
Core-1 Core-2
St a = x
while (a==x){}
fence
St b = y

## Slide 31: Root cause – barrier semantics
SO
Ordering + Completion
  High latency
Completion not always necessary [Chidambaram ‘13]
Buffered persistency [Pelley ’14]
Ordering only
  Low latency
  Pipeline persists

## Slide 32: SO example
Objective: persist A and B in order
St A = x
CLWB A
fence
PCOMMIT
fence
St B = y
Barrier
(1) Ensures `A’ is accepted to MC before PCOMMIT
(2) Ensures `B’ cannot reach cache before `A’ persists
(1) + (2) => A and B persist in order

## Slide 33: The dark side of PCOMMIT
St A = x
CLWB A
fence
PCOMMIT
fence
St B = y
Barrier
(1) Ensures `A’ is accepted to MC before PCOMMIT
(2) Ensures `B’ cannot reach cache before `A’ persists
Exposes PM latency to the core on every PCOMMIT
Frequent processor stalls

## Slide 34: Recent developments
Intel deprecated PCOMMIT 4 weeks ago
Requires a persistent write queue at MC
Cores
Caches
Mem Ctrl
PM
Persistent
domain

## Slide 35: SO example revisited
Objective: persist A and B in order
St A = x
CLWB A
Sfence
St B = y
Ensures `A’ is accepted to MC before `B’ reaches cache
MC access latency still exposed to core (vs PM latency)
1.5x slowdown vs 7.3x

## Slide 36: RCBSP
Relaxed Consistency Buffered Strict Persistency
Relaxed consistency
  We use ARM v7a
Strict persistency
  Persist order = Store order
Buffering
/* Init: a = 0, b=0
a,b are persistent */
Core-1 Core-2
St a = x
while (a==0){}
dmb
St b = y
St a <m St b  St a <p St b

## Slide 37: Delegated Persist Ordering
Aasheesh Kolli Jeff Rosen Stephan Diestelhorst Ali Saidi
Steven Pelley Sihang Liu Peter M. Chen Thomas F. Wenisch
MICRO 2016 - Taipei
Notes: Good morning everyone, I am Aasheesh Kolli from the university of michigan, and today I am going to talk about how to design transactions for future persistent memory enable systems.

## Slide 38: Delegated Persist Ordering
Aasheesh Kolli Jeff Rosen Stephan Diestelhorst Ali Saidi
Steven Pelley Sihang Liu Peter M. Chen Thomas F. Wenisch
MICRO 2016 - Taipei
Notes: Good morning everyone, I am Aasheesh Kolli from the university of michigan, and today I am going to talk about how to design transactions for future persistent memory enable systems.

## Slide 39: Performance
Chart: Normalized execution time
| Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | Cqueue | Aswap | TATP | RBTree | TPCC | GMEAN | PCM | DRAM | PWQ
SO | 5.7143 | 34.7917 | 15.7006 | 1.3382 | 4.9969 | 7.3099 | 2.9667 | 6.2771 | 3.9218 | 1.1745 | 3.019 | 3.0384 | 2.1587 | 1.8631 | 1.7232 | 1.1204 | 1.2921 | 1.5859
RCBSP | 1.746 | 4.5536 | 2.9322 | 1.0224 | 1.6249 | 2.0778 | 1.35 | 1.3193 | 1.067 | 1.0118 | 1.2896 | 1.1992 | 1.3016 | 1.3631 | 1.0791 | 1.012 | 1.3497 | 1.212
35
16
* Execution times normalized to volatile execution
?
Execution times down with lower memory latencies
Array swaps, most write intensive, suffers the most, except …
Concurrent queue, thread contention exposes CLWBs
RB tree, least write intensive, dominated by volatile execution
RCBSP, consistently out performs SO for all mem configs
3.5x
2.5x
1.3x

## Slide 40: Memory persistency models
Allow programmers to express write order to PM
Hardware responsible for enforcing write order
Similar to memory consistency models
Synchronous Ordering (SO) – based on [Intel ‘15]

## Slide 41: SO barrier v. RCBSP barrier
SO (based on [Intel ‘15])
Ordering + Completion
  Stronger guarantee
  Easier to reason
  Potentially fewer barriers
Conservative stalling
  Completion not always req.
Synchronous barrier
RCBSP [Pelley ‘14]
Ordering only (mostly)
  Weaker guarantee
  Harder to reason
  Potentially more barriers
Stall when no buffer space
  Ordering mostly sufficient
Delegation barrier

## Slide 42: Barriers in action
Synchronous: Epoch-1 persists before Epoch-2 begins
Delegation: Epoch-1 ordered to persist before Epoch-2
Core
$
E1
E2
Core
$
E1
E2
Time
Finish
Time
Finish
>