## Slide 1: Enabling Ultra Low Voltage System Operation by Tolerating On-Chip Cache Failures
August 20, 2009
Amin Ansari, Shuguang Feng, Shantanu Gupta, and Scott Mahlke
Advanced Computer Architecture Lab.
University of Michigan, Ann Arbor

## Slide 2
Motivation
    Extreme technology integration in sub-micron regime
      Heat dissipation ↑ and power density ↑
        Cost of thermal packaging, cooling, and electricity ↑
        Device lifetime ↓
    If high performance is not needed  DVS
      Improvement in battery life of medical devices, laptops, and etc
    Large SRAM structures limit the min achievable Vdd
      because SRAM delay increases at a higher rate than CMOS logic delay as Vdd is decreased

## Slide 3
Bit-Error-Rate for an SRAM Cell
    Extremely fast growth in failure rate with decreasing Vdd
    Due to systematic and random process variation
      Min sustainable Vdd of entire cache is determined by the one SRAM bit-cell with the highest required operational voltage
    Min achievable Vdd for 64KB and 2MB caches
      In 90nm while targeting 99% yield
    Write-margin of L2 cache determines the min Vdd

## Slide 4
Our Goal
    Enabling DVS to push core’s Vdd down to
      Ultra low voltage region ( < 600mV )
      While preserving correct functionality of on-chip caches
    Proposing a highly flexible and FT cache architecture that can efficiently tolerate these SRAM failures
    No gain in high power mode
      Minimizing our overheads in this mode
      Single power supply, because dual Vdd have
        Area and design complexity ↑
        Necessity of voltage converters
        Large noise from the high voltage island

## Slide 5
Our Fault-Tolerant Cache
    Interweaving a set of n+1 partially functional cache word-lines to give the appearance of n functional lines
    Partitioning the set of all lines into large groups
      One line per group serves as redundancy for other lines
      Each line is divided to multiple chunks (smaller redundancy units)
      Two lines have collision, if they have at least one faulty chunk in the same position (10 and 15 are collision free)
    We form groups such that there are no collision between any two lines within a group
      Group 3 (G3) contains lines 4, 10, and 15

## Slide 6
Architecture
MUXing layer
1
3
5
7
2
4
6
8
First Bank
Second Bank
G3(S)
Functional Block
G3
1
Fault Map
-
-
2
G3(1)
G3(2)
15
4
G3
2
Input Address
9
11
13
15
10
12
14
16
Data line
Sacrificial line
Fault map address
Group address of data line
Memory Map
Added modules:
+ Memory map
+ Fault map
+ MUXing layer
Two type of lines:
+ data line
+ sacrificial line

## Slide 7
Group Formation
1
3
5
7
2
4
6
8
G1(S)
9
11
13
15
10
12
14
16
G2(1)
G2(2)
G3(S)
G4(1)
G4(2)
G4(3)
G5(S)
G1(1)
G2(S)
G1(2)
G4(S)
G3(1)
G3(2)
D
G5(1)
1
G1(S)
9
11
G1(1)
G1(2)
3
2
10
G2(1)
G2(2)
G2(S)
4
13
14
G3(S)
G3(1)
G3(2)
5
7
6
12
G4(1)
G4(2)
G4(3)
G4(S)
8
16
G5(S)
G5(1)
cache fault
pattern
Group
1
Group 2
Group
3
Group
4
Group
5

## Slide 8
Operation Modes
    Low power mode (Vdd < 651mV)
      First time processor switches to this mode
        BIST scans cache for potential faulty cells
        Processor switches back to high power mode
        Forms groups and fills the memory and fault maps
    High power mode (Vdd ≥ 651mV)
      Our scheme is turned off to minimize overheads
        There is no sacrificial lines in this case
        Clock gating to reduce dynamic power of SRAM structures
        Bypass MUXes still burn dynamic power
        No power gating is used for leakage mitigation

## Slide 9
Evaluation Methodology
    Performance
      SimAlpha that is based on SimpleScalar OoO
      Processor is modeled after DEC EV-7
    Delay, power and area
      CACTI for caches and other SRAM structures
      Synopsys standard tool-chain for
        Miscellaneous logic (e.g. bypass MUXes and comparators)
    Given set of cache parameters (e.g. Vdd)
      Monte Carlo (with 1000 iterations) using described algorithm
      Determining disabled portion of caches (for 99% yield)

## Slide 10
Minimum Achievable Vdd
    Protecting L2 is harder than L1
      Due to longer lines and larger size
      Chunk size = 8b for L2 and 4b for L1
      Achieving 420mV by enforcing the following 10% limits

## Slide 11
Overheads
    Overheads for L1 and L2 caches
      10T used to protect fault map, tag array, and memory map
    Using SPEC2K benchmark suite
      INT: (gzip, vpr, gcc, mcf, crafty, parser, vortex, bzip2, twolf)
      FP: (swim, mgrid, applu, art, equake, ammp, sixtrack)
      4.7% performance penalty for EV-7 (simAlpha)

## Slide 12
Conclusion
    DVS is widely used to deal with high power dissipation
      Minimum achievable voltage is bounded by SRAM structures
    We proposed a flexible FT cache architecture
      To tolerate these SRAM failures efficiently when operating in low power mode
    Using our approach
      Operational voltage of processor can be reduced to 420mV
      80% dynamic power saving and 73% leakage power saving
      4.7% performance overhead for microprocessor
      < 15% overhead for on-chip caches