## Slide 1
Andrew Canis, Jongsok Choi, Mark Aldham, Victor Zhang, Ahmed Kammoona, Jason Anderson, Stephen Brown, and Tomasz Czajkowski
Presented by: Hasan Al Maruf, Harisankar Sadasivan, Sheng Chong, Fan Lai
LegUp High-Level Synthesis for FPGA-Based Processor/Accelerator Systems
Andrew Canis, Jongsok Choi, etl
University of Toronto
Presented by: Hasan Al Muraf, Harisankar Sadasivan, Sheng Chong, Fan Lai

## Slide 2: Hardware design has advantages over software
Reason: Significant performance/energy-efficiency boost from hardware accelerators
Chart: Heterogeneous computing system in Top500
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 (June)
Accelerators/Co-processors Systems | 1 | 8 | 7 | 17 | 39 | 62 | 53 | 75 | 102 | 94
Notes: As we know that OpenCL is an open standard for programing heterogeneous computing systems,
and these systems are becoming more and more popular in the Top500 list.
People are putting accelerators like GPU/Xeon PHI into they supercomputers
because these accelerators deliver better performance and energy-efficiency

## Slide 3
Issues
Hardware design is difficult and skills are rare:
  Complex RTL codes
  Difficult to debug
  Costly
Unique Accelerator for a single application?

## Slide 4
Application-Specific Accelerator with FPGA
Only provides primitive building blocks for computation
  Register, add/mul, memories, boolean operations and connections
Build application-specific accelerator from primitives building blocks
  Interconnection between primitive functional units
  Timing of data movement between primitive functional units
Opportunities for optimizations for a specific application
  Maximizing efficiency while throwing away redundancy
Notes: And FPGAs allow us to create such accelerators,
<next>
Specifically, FPGAs provides primitive building blocks for computation,
<next>
from these building blocks, the users can build they own accelerator for their applications
With this fine-grain programmability
<next>
Such a fine-grain programmability from those primitive building blocks,
Provide the opportunities to optimize the accelerator for a given application,
For every single bit and every single clock cycle
This allow the users to maximize efficiency while minimizing redundancy in the accelerator

## Slide 5
Performance/Power at different levels of specialization
CPU
FPGA
ASIC
(not programmable)
GPU
https://en.bitcoin.it/wiki/Non-specialized_hardware_comparison
https://en.bitcoin.it/wiki/Mining_hardware_comparison
Notes: Lets takes the bitcoin mining hardware as an example, We should the power and performance comparison in this graph
We have CPU, GPU, FPGA and the application-specific integrated-circuit, which also known as ASIC
And among all those programmable devices, FPGAs deliver the best performance and energy-efficiency.
Because people built optimal processing pipeline for bitcoin mining from FPGAs,
In such a pipeline, almost every bit, every computations are designed to do bitcoin mining only,
And this application-level specialization deliver the best performance and and energy-efficiency
-------
As we can see that the ASIC delivers the best performance and energy-efficiency.
FPGA provide the best performance and energy-efficiency
It is how you design that matter
CNN five years ago?
CNN two years ago?

## Slide 6: Challenges of promoting FPGAs among software engineers
Require tremendous efforts
Extensive knowledge of digital circuit design
The potential of FPGAs is not easily accessible by common software engineers
Solution? - High Level Synthesis (HLS) frameworks
AXI Master
Burst inference
DSP48
Timing Closure
Stable interface
Loop rewind
Notes: But designing such an optimal pipeline for a given application requires tremendous efforts,
<next>
As well as extensive digital circuit design knowledge
<next>
For example, all these words,
<next>
Just sounds like magical spells for most of the software developers
<next>
As a result, the potential of FPGAs is not easily accessible by common software engineers,
And we want to change this
---
Fpga – spatial expension – pipeline parallelism, internal memory bandwidth – advantage over gpu – and weakness – memory band width

## Slide 7: Existing Frameworks
Framework | Non Commercial License | Source Code Modifiable | Domain Independent
Trident |  |  | 
ROCCC |  |  | 
xPilot |  |  | 
GAUT |  |  | 
WrapProcessor |  |  | 
LiquidMetal |  |  | 
CHiMPS |  |  | 
LegUp |  |  | 
Notes: But designing such an optimal pipeline for a given application requires tremendous efforts,
<next>
As well as extensive digital circuit design knowledge
<next>
For example, all these words,
<next>
Just sounds like magical spells for most of the software developers
<next>
As a result, the potential of FPGAs is not easily accessible by common software engineers,
And we want to change this
---
Fpga – spatial expension – pipeline parallelism, internal memory bandwidth – advantage over gpu – and weakness – memory band width

## Slide 8: LegUP
Program code
C Compiler
Processor
(MIPS)
Self-Profiling
Processor
Profiling Data:
Execution Cycles
Power
Cache Misses
High-level synthesis
Suggested
program segments to target to HW
FPGA fabric
mP
Hardened program segments
Altered SW binary (calls HW accelerators)
int FIR(int ntaps, int sum) {
int i;
for (i=0; i < ntaps; i++)
sum += h[i] * z[i];
return (sum);
}
....

## Slide 9
System Architecture
FPGA
MIPS Processor
Hardware Accelerator
AVALON INTERFACE
Hardware Accelerator
Memory Controller
On-Chip Cache Memory
Off-Chip Memory

## Slide 10
High-Level Synthesis Flow
C Compiler (LLVM)
C Program
Allocation
Scheduling
Binding
Target H/W Characterization
RTL Generation
User Constraints
Timing
Resource
Synthesizable Verilog
Optimized LLVM IR
Assign operations to states
Decide sharing strategies
Hardware pre-characterization

## Slide 11
LLVM Compiler
Compile C code into IR
  Simple enough to correspond to HW operations
LLVM performs standard optimizations
  SSA & Alias analysis for dependency analysis.
Data
Memory
Notes: The advantage of stalling is energy consumption – the processor is in a low-power state while the accelerator operates. we use only mode #2 (stalling) for the results in this paper

## Slide 12
Allocation: Profile the H/W
Goal: Set-up constraints for subsequent synthesis steps
Characterize HW resource
  Read HW information from configuration TCL files
  Pre-characterize hardware operation for each instruction
Make early predictions for scheduling and binding
  Circuit speed, area for HW accelerators
Notes: The advantage of stalling is energy consumption – the processor is in a low-power state while the accelerator operates. we use only mode #2 (stalling) for the results in this paper

## Slide 13
Scheduling: CFG to FSM
Goal: assign operations to clock cycles (states) & build FSM.
Legup schedules basic blocks individually
  ASAP scheduling policy
Operation chaining
  Schedule an instruction into the same state as its operand
  When estimated delay of chain operations doesn’t exceed clock period
  Reduce HW latency, save registers w/o impacting final clock period
OP 1
OP 2
1 CLK period
Notes: The advantage of stalling is energy consumption – the processor is in a low-power state while the accelerator operates. we use only mode #2 (stalling) for the results in this paper

## Slide 14
Binding: Map operation to FU
Goal: save area as much as possible
  Sharing functional units between actions -> operation assignment
  Sharing registers/memories between variables -> register allocation
FPGA fabric is register rich, but multiplexers are expensive
How to bind?
  Weighted bipartite matching problem
Notes: The advantage of stalling is energy consumption – the processor is in a low-power state while the accelerator operates. we use only mode #2 (stalling) for the results in this paper

## Slide 15
Binding: Weighted bipartite Matching Problem
LLVM operation
Functional Units
How to assign weights?
Notes: The advantage of stalling is energy consumption – the processor is in a low-power state while the accelerator operates. we use only mode #2 (stalling) for the results in this paper

## Slide 16
Goal: Assign penalty weights in following priority to derive a cost function
New MUX I/P (+1)
Existing MUX I/P (+0.1)
Sharing O/P register (-0.1)
How do you optimize the cost Function?
Use bipartite Matching
Binding

## Slide 17
Local Accelerator Memories
Shared memory between processor and accelerators
Create local memory for constants/local variables
  Avoid contentions
Multiple memories for better parallelism

## Slide 18
Pointer Example
Each local memory is assigned a 9-bit tag
  Top 9 bits of the 32-bit address space
  To steer memory access

## Slide 19
Non-intrusive & Real-time Hardware Profiling
Performs analysis at function level
Works by associating an index and a counter with a function
6.7% overhead on MIPS processor area

## Slide 20
Processor/Accelerator Communication
While waiting, the processor
  Continue running but periodically check
  Or totally stall
Wrapper
  Replace target function for HW implementation
  Pass arguments to HW
  Assert start signal
  Wait for return data
Notes: The advantage of stalling is energy consumption – the processor is in a low-power state while the accelerator operates. we use only mode #2 (stalling) for the results in this paper

## Slide 21
Benchmarks
More supports than existing HLS
  Additional support for structs, global variables, pointer arithmetic
64-bit double precision are implemented using integer types
Various categories in benchmarks

## Slide 22: Evaluations
Metrics
Speed: total execution time
Area: # of used logic elements, memory bits, multipliers
Energy cost
Baselines
Pure H/W implementation
  eXcite-based Hardware, Legup-based Hardware
Pure Software
Hybrid implementation: Legup-based Software & Hardware

## Slide 23: Evaluations: Execution Time
Benchmark | Pure SW
Dfadd | 222
Motion | 495
Gsm | 527
JPEG decoder | 401328
eXCite | Legup
15 | 19
53 | 93
113 | 137
143358 | 124475
Legup-based Hybrid
68
203
303
342511
SW + HW
Pure HW
Pure SW
Pure HW implementation outperforms SW
Legup is comparable to eXCite

## Slide 24: Evaluations: Execution Time & Area
Two SW-HW hybrids
  H1: offload the most comp-utation intensive function
  H2: offload the 2nd most computation intensive func
Less execution time with more HW implementations
  Legup ~ eXCite
SW
Legup
eXCite
H2
H1

## Slide 25: Evaluations: Energy Cost
SW
Legup
eXCite
H2
H1
Two SW-HW hybrids
  H1: offload the most comp-utation intensive function
  H2: offload the 2nd most computation intensive func
Less energy cost as more HW-based implementations
  Legup ~ eXCite
18x less energy than software

## Slide 26: Contribution & Weakness
A powerful open source platform for HLS research
  Great improvement for energy cost & speed
  Custom HLS passes add-on option
  Domain-generalized
Weakness
  Still limited support
  Performance is decent, but not impressive

## Slide 27: Open questions
Pure HW implementation is the best in evaluations
  Any concerns on this ?
  Difficult to debug in HW
  Performance-budget trade-off

## Slide 28: Thanks! Q&A

## Slide 29
Evaluation

## Slide 30
Binding: Bipartite Matching
How do you optimize the cost for the party

## Slide 31
Binding: Hungarian Method for BP Subtract the smallest value in each row from the other values in the row:
1. Form an adjacency matrix.

## Slide 32
Binding: Hungarian Method for BP
2. Subtract the smallest value in each row from the other values in the row.

## Slide 33
Binding: Hungarian Method for BP
3. Subtract the smallest value in each column from the other values in the column.

## Slide 34
Binding: Hungarian Method for BP
4. Draw lines through the rows and columns that have the 0 entries
such that fewest possible lines are drawn.
Two lines drawn & 2 < 3, hence there is not yet the optimal no. of zeroes.

## Slide 35
Binding: Hungarian Method for BP
5. Find smallest entry not covered by any line.
Subtract this from uncovered rows.

## Slide 36
Binding: Hungarian Method for BP
6. Add the same value to the covered columns.

## Slide 37
Binding: Hungarian Method for BP
7. Draw minimum lines through rows and columns of 0

## Slide 38
Binding: Hungarian Method for BP
8. 3 lines, so done.
Assignments are where only 1 zero per row and column
Is a part of assignment.

## Slide 39
Binding: Hungarian Method for BP
9. Replace original values.