## Slide 1: A Trusted Safety Verifier for Process Controller Code
Stephen McLaughlin, Saman Zonouz, Devin Pohly, Patrick McDaniel
Presented by Xumiao Zhang and Shenghao Lin
Notes: 1-9 10-18 19-21 22-26 27-28

## Slide 2: Overview
Programmable logic controller (PLC)
Threat model
Trusted Safety Verifier (TSV)
PLC code analysis
Implementation
Evaluation
Conclusion

## Slide 3: Programmable Logic Controller
A Programmable Logic Controller (PLC) is a digital, multi- input multi-output computer used for real-time automation of physical machinery.
A PLC’s program is executed continuously as long as the PLC is running.

## Slide 4: A PLC’s Life
Turn left 2˚
Turn left!

## Slide 5: A PLC’s Life
Turn left 2˚
Turn left!
1º

## Slide 6: A PLC’s Life
Not quite...
Turn left!
1º

## Slide 7: A PLC’s Life
Not quite...
Turn left!
2º

## Slide 8: A PLC’s Life
BINGO!
Stop!
2º

## Slide 9: A PLC’s Life
Control Signal
Sensor Measurements
L DW2 ;; Degrees
< ID255
ST Q 3.2
Control Logic
Scan Cycle

## Slide 10: Bad news...
Programmable Controllers are insecure by design
Control systems are not robust enough for security patches (i.e. stuxnet)

## Slide 11: A PLC’s Life
;; Spin out
;; of control!
S Q 3.2
Control Logic

## Slide 12: Safety Properties
Bounds on numerical device parameters (e.g. maximum drive velocity and acceleration)
Safety interlocks, which ensure physically conflicting events do not occur.

## Slide 13: Trusted Safety Verifier (TSV)
Goal: Only allow code to be run on a PLC if it satisfies a set of engineer-supplied safety properties.

## Slide 14: TSV - Challenges
Existing tools not up to the task.
Control systems are stateful, requiring temporal properties.
State space explosion with existing analysis techniques.

## Slide 15: TSV - Architecture

## Slide 16: Sample PLC Code
AI 0.5 ;; And input bit 5
=Q 0.1 ;; Store at output bit 1

## Slide 17: Instruction List Intermediate Language
Side effects
PLC special features
Architecture dependent

## Slide 18: Instruction List Intermediate Language
PLC Code

## Slide 19: Symbolic Execution
TSV symbolically executes an ILIL program to produce a mapping from path predicates to symbolic outputs.
Symbolic execution follows all possible paths through a single scan cycle of the program.
Lump together all inputs that produce that same output.

## Slide 20: Symbolic Execution - Example
Without symbolic execution, an unsigned integer input can generate 2^32 different states.
With symbolic execution, only 2 states.
if input > 10 then output input + 6
else output 2 * input + 6
Notes: We will see its use later.

## Slide 21: Symbolic Execution - Expression

## Slide 22: Checking Temporal Properties
PLCs use stateful variables, which retain their values across the scan cycles.
TEG (temporal execution graph) is applied for model checking.

## Slide 23: Temporal Execution Graph (TEG)
A state machine in which each state transition represents a single scan cycle.
Each state in the TEG contains the state and output variables.

## Slide 24: TEG

## Slide 25: TEG with Symbolic Execution

## Slide 26: TSV - A Full Run

## Slide 27: Conclusion
Developed Trusted Safety Verifier (TSV), a trusted verification platform for programmable logic controllers.
  last-step security verification of control commands
  Combination of symbolic execution and model checking
Implemented a real-world prototype of the TSV framework on an independent Raspberry PI chip with minimal attack surface.
  Demonstrated performance in checking various properties in control systems