## Slide 1: EECS 583 – Class 13 Software Pipelining
University of Michigan
February 20, 2023

## Slide 2: Announcements + Reading Material
Next week is Spring Break, no class Feb 27 & Mar 1
Project discussion meetings – Mar 6, 8, 9 (10am-noon each day)
  Each group meets 10 mins with Aditya and I on Zoom
  Action items
    Form or join a team (3-4 people per team)
    Use piazza to recruit additional group members or express your availability
    Project areas, start looking for research papers, think about the specifics
  Google calendar signup available – see piazza post by Aditya – Please just sign up once!
Project proposals
  Due Monday, Mar 13, midnight
  1 paragraph summary of what you plan to work on
    Topic, what are you going to do, what is the goal, 1-2 references
  Email to me & Aditya, cc all your group members
Today’s class reading
  “Code Generation Schema for Modulo Scheduled Loops”, B. Rau, M. Schlansker, and P. Tirumalai, MICRO-25, Dec. 1992.
Next class
  “Register Allocation and Spilling Via Graph Coloring,” G. Chaitin, Proc. 1982 SIGPLAN Symposium on Compiler Construction, 1982.

## Slide 3: Recap: Dynamic Single Assignment (DSA) Form
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
Impossible to overlap iterations because each iteration writes to the same
register. So, we’ll have to remove the anti and output dependences.
Virtual rotating registers
* Each register is an infinite push down array (Expanded virtual reg or EVR)
* Write to top element, but can reference any element
* Remap operation slides everything down  r[n] changes to r[n+1]
A program is in DSA form if the same virtual register (EVR element) is never
assigned to more than 1x on any dynamic execution path
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
6: p1[-1] = cmpp (r1[-1] < r9)
remap r1, r2, r3, r4, p1
7: brct p1[-1] Loop
DSA
conversion

## Slide 4: Loop Dependence Example
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
6: p1[-1] = cmpp (r1[-1] < r9)
remap r1, r2, r3, r4, p1
7: brct p1[-1] Loop
1
2
3
4
5
6
7
In DSA form, there are no
inter-iteration anti or output
dependences!
Assume compiler can prove load and store are never dependent
1,0
1,0
0,0
3,0
2,0
1,1
1,1
1,1
1,1
0,0
<delay, distance>
r1 = &A
r2 = &B
Loop:

## Slide 5: Class Problem
1: r1[-1] = load(r2[0])
2: r3[-1] = r1[1] – r1[2]
3: store (r3[-1], r2[0])
4: r2[-1] = r2[0] + 4
5: p1[-1] = cmpp (r2[-1] < 100)
remap r1, r2, r3
6: brct p1[-1] Loop
Draw the dependence graph
showing both intra and inter
iteration dependences
Latencies: ld = 2, st = 1, add = 1, cmpp = 1, br = 1
1
2
3
4
5
6

## Slide 6: Class Problem Answer
1: r1[-1] = load(r2[0])
2: r3[-1] = r1[1] – r1[2]
3: store (r3[-1], r2[0])
4: r2[-1] = r2[0] + 4
5: p1[-1] = cmpp (r2[-1] < 100)
remap r1, r2, r3
6: brct p1[-1] Loop
Draw the dependence graph
showing both intra and inter
iteration dependences
Latencies: ld = 2, st = 1, add = 1, cmpp = 1, br = 1
1
2
3
4
5
6
1
2
3
4
5
6
<0,0>
<2,3>
<2,2>
<1,0>
<1,1>
<1,1>
<1,0>
<1,0>
<1,1>
<0,0>
Instructions 1-5 have <0,0>
control dependences to 6.
<1,0>
<1,1>
Red edges are memory anti and flow dependences

## Slide 7: Minimum Initiation Interval (MII)
Remember, II = number of cycles between the start of successive iterations
Modulo scheduling requires a candidate II be selected before scheduling is attempted
  Try candidate II, see if it works
  If not, increase by 1, try again repeating until successful
MII is a lower bound on the II
  MII = Max(ResMII, RecMII)
  ResMII = resource constrained MII
    Resource usage requirements of 1 iteration
  RecMII = recurrence constrained MII
    Latency of the circuits in the dependence graph

## Slide 8: ResMII
Simple resource model
A processor has a set of resources R. For each resource r in R
there is count(r) specifying the number of identical copies
Concept: If there were no dependences between the operations, what
is the the shortest possible schedule?
ResMII = MAX (uses(r) / count(r))
for all r in R
uses(r) = number of times the resource is used in 1 iteration
In reality its more complex than this because operations can have
multiple alternatives (different choices for resources it could be
assigned to), but we will ignore this for now

## Slide 9: ResMII Example
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
ALU: used by 2, 4, 5, 6
 4 ops / 2 units = 2
Mem: used by 1, 3
 2 ops / 1 unit = 2
Br: used by 7
 1 op / 1 unit = 1
ResMII = MAX(2,2,1) = 2
ResMII = MAX (uses(r) / count(r))
uses(r) = number of times the resource is used in 1 iteration

## Slide 10: RecMII
Approach: Enumerate all irredundant elementary circuits in the
dependence graph
RecMII = MAX (delay(c) / distance(c))
for all c in C
delay(c) = total latency in dependence cycle c (sum of delays)
distance(c) = total iteration distance of cycle c (sum of distances)
2
1
1,0
3,1
cycle
k 1
k+1 2
k+2
k+3
k+4 1
k+5 2
1
3
4 cycles,
RecMII = 4
delay(c) = 1 + 3 = 4
distance(c) = 0 + 1 = 1
RecMII = 4/1 = 4

## Slide 11: RecMII Example
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
1
2
3
4
5
6
7
1,0
1,0
0,0
3,0
2,0
1,1
1,1
1,1
1,1
0,0
<delay, distance>
4  4: 1 / 1 = 1
5  5: 1 / 1 = 1
4  1  4: 1 / 1 = 1
5  3  5: 1 / 1 = 1
RecMII = MAX(1,1,1,1) = 1
Then,
MII = MAX(ResMII, RecMII)
MII = MAX(2,1) = 2
RecMII = MAX(delay(c) / distance(c))
delay(c) = total latency in dependence cycle c (sum of delays)
distance(c) = total iteration distance of cycle c (sum of distances)

## Slide 12: Homework Problem
1: r1[-1] = load(r2[0])
2: r3[-1] = r1[1] – r1[2]
3: store (r3[-1], r2[0])
4: r2[-1] = r2[0] + 4
5: p1[-1] = cmpp (r2[-1] < 100)
remap r1, r2, r3
6: brct p1[-1] Loop
Calculate RecMII, ResMII, and MII
Latencies: ld = 2, st = 1, add = 1, cmpp = 1, br = 1
Resources: 1 ALU, 1 MEM, 1 BR
1
2
3
4
5
6
<0,0>
<2,3>
<2,2>
<1,0>
<1,1>
<1,1>
<1,0>
<1,0>
<1,1>
<0,0>

## Slide 13: Modulo Scheduling Process
Use list scheduling but we need a few twists
  II is predetermined – starts at MII, then is incremented
  Cyclic dependences complicate matters
    Estart/Priority/etc.
    Consumer scheduled before producer is considered
      There is a window where something can be scheduled!
  Guarantee the repeating pattern
2 constraints enforced on the schedule
  Each iteration begin exactly II cycles after the previous one
  Each time an operation is scheduled in 1 iteration, it is tentatively scheduled in subsequent iterations at intervals of II
    MRT used for this

## Slide 14: Priority Function
Height-based priority worked well for acyclic scheduling, makes sense
that it will work for loops as well
Acyclic:
Height(X) =
0, if X has no successors
MAX ((Height(Y) + Delay(X,Y)), otherwise
for all Y = succ(X)
Cyclic:
HeightR(X) =
0, if X has no successors
MAX ((HeightR(Y) + EffDelay(X,Y)), otherwise
for all Y = succ(X)
EffDelay(X,Y) = Delay(X,Y) – II*Distance(X,Y)

## Slide 15: Calculating Height
1
2
3
4
3,0
1,1
2,2
Insert pseudo edges from all nodes to branch with latency = 0, distance = 0 (dotted edges)
Compute II, For this example assume II = 2
HeightR(4) =
HeightR(3) =
HeightR(2) =
HeightR(1)
2,0
0,0
0,0
0,0

## Slide 16: Calculating Height Solution
1
2
3
4
3,0
1,1
2,2
Insert pseudo edges from all nodes to branch with latency = 0, distance = 0 (dotted edges)
Compute II, For this example assume II = 2
HeightR(4) = H(4) + (1 – II*1) (Assume H(4) is 0 since not calculated yet 0 + 1-2 = -1  0 (Always MAX answer with 0)
HeightR(3) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(2) + 2 – II*2 = 0 + 2 – 2*2 = -2) Assume H(2) is 0 since not calculated yet = 0
HeightR(2) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(3) + 2 – II*0 = 0 + 2 – 2*0 = 2) = 2
HeightR(1) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(2) + 3 – II*0 = 2 + 3 – 2*0 = 5) = 5
Now recalculate the heights to see if anything changes since HeightR(3) assumed wrong value for node 2 HeightR(3) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(2) + 2 – II*2 = 2 + 2 – 2*2 = 0) = 0  Unchanged, so no need to compute any other heights again
2,0
0,0
0,0
0,0

## Slide 17: The Scheduling Window
E(Y) =
0, if X is not scheduled
MAX (0, SchedTime(X) + EffDelay(X,Y)),
otherwise
With cyclic scheduling, not all the predecessors may be scheduled,
so a more flexible earliest schedule time is:
MAX
for all X = pred(Y)
Latest schedule time(Y) = L(Y) = E(Y) + II – 1
Every II cycles a new loop iteration will be initialized, thus every II
cycles the pattern will repeat. Thus, you only have to look in a
window of size II, if the operation cannot be scheduled there, then
it cannot be scheduled.
where EffDelay(X,Y) = Delay(X,Y) – II*Distance(X,Y)

## Slide 18: Loop Prolog and Epilog
Prolog
Epilog
Kernel
Only the kernel involves executing full width of operations
Prolog and epilog execute a subset (ramp-up and ramp-down)
II = 3

## Slide 19: Removing Prolog/Epilog
Prolog
Epilog
Kernel
II = 3
Disable using
predicated execution
Execute loop kernel on every iteration, but for prolog and epilog
selectively disable the appropriate operations to fill/drain the pipeline

## Slide 20: Kernel-only Code Using Rotating Predicates
A0
A1 B0
A2 B1 C0
A B C D
Bn Cn-1 Dn-2
Cn Dn-1
Dn
P[0] P[1] P[2] P[3]
1 0 0 0
1 1 0 0
1 1 1 0
1 1 1 1
…
0 1 1 1
0 0 1 1
0 0 0 1
A if P[0] B if P[1] C if P[2] D if P[3]
A - - -
A B - -
A B C -
A B C D
…
- B C D
- - C D
- - - D
P referred to as the staging predicate

## Slide 21: Modulo Scheduling Architectural Support
Loop requiring N iterations
  Will take N + (S – 1) where S is the number of stages
2 special registers created
  LC: loop counter (holds N)
  ESC: epilog stage counter (holds S)
Software pipeline branch operations
  Initialize LC = N, ESC = S in loop preheader
  All rotating predicates are cleared
  SWP-BR (BRF)
    While LC > 0, decrement LC and RRB, P[0] = 1, branch to top of loop
      This occurs for prolog and kernel
    If LC = 0, then while ESC > 0, decrement RRB and write a 0 into P[0], and branch to the top of the loop
      This occurs for the epilog

## Slide 22: Execution History With LC/ESC
LC ESC P[0] P[1] P[2] P[3]
3 3 1 0 0 0 A
2 3 1 1 0 0 A B
1 3 1 1 1 0 A B C
0 3 1 1 1 1 A B C D
0 2 0 1 1 1 - B C D
0 1 0 0 1 1 - - C D
0 0 0 0 0 1 - - - D
A if P[0]; B if P[1]; C if P[2]; D if P[3]; P[0] = BRF;
LC = 3, ESC = 3 /* Remember 0 relative!! */
Clear all rotating predicates
P[0] = 1
4 iterations, 4 stages, II = 1, Note 4 + 4 –1 iterations of kernel executed

## Slide 23: Modulo Scheduling Example
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
for (j=0; j<100; j++)
b[j] = a[j] * 26
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
7: brlc Loop
Loop:
Loop:
LC = 99
Step1: Compute to loop into
form that uses LC

## Slide 24: Example – Step 2
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step 2: DSA convert
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
7: brlc Loop
Loop:
LC = 99

## Slide 25: Example – Step 3
1
2
3
4
5
7
1,1
3,0
2,0
1,1
1,1
1,1
1,1
RecMII = 1
RESMII = 2
MII = 2
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step3: Draw dependence graph
Calculate MII
0,0
0,0
No memory dependences since load and store refer to distinct arrays

## Slide 26: Example – Step 4
1: H = 5
2: H = 3
3: H = 0
4: H = 0
5: H = 0
7: H = 0
1
2
3
4
5
7
1,1
0,0
3,0
2,0
1,1
1,1
1,1
1,1
Step 4 – Calculate priorities (MAX height
to pseudo stop node)
0,0
0,0
0,0
0,0
0,0
0,0
1: H = 5
2: H = 3
3: H = 0
4: H = 4
5: H = 0
7: H = 0
Iter1
Iter2

## Slide 27: Example – Step 5
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Schedule brlc at time II - 1
alu0
alu1
mem
br
MRT
0
1
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
0
1
2
3
4
5
6

## Slide 28: Example – Step 6
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step6: Schedule the highest priority op
Op1: E = 0, L = 1
Place at time 0 (0 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
0
1
2
3
4
5
6

## Slide 29: Example – Step 7
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step7: Schedule the highest priority op
Op4: E = 0, L = 1
Place at time 0 (0 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
4
4
0
1
2
3
4
5
6

## Slide 30: Example – Step 8
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step8: Schedule the highest priority op
Op2: E = 2, L = 3
Place at time 2 (2 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
4
4
2
2
X
0
1
2
3
4
5
6

## Slide 31: Example – Step 9
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step9: Schedule the highest priority op
Op3: E = 5, L = 6
Place at time 5 (5 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
2
2
3
3
X
4
4
X
0
1
2
3
4
5
6

## Slide 32: Example – Step 10
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step10: Schedule the highest priority op
Op5: E = 5, L = 6
Place at time 5 (5 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
2
2
3
3
X
4
4
X
5
X
5
0
1
2
3
4
5
6

## Slide 33: Example – Step 11
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step11: calculate ESC, SC = ceiling(max unrolled sched length / ii)
unrolled sched time of branch = rolled sched time of br + (ii*esc)
SC = 6 / 2 = 3, ESC = SC – 1
time of br = 1 + 2*2 = 5
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
2
2
3
3
X
4
4
X
5
X
5
7
0
1
2
3
4
5
6

## Slide 34: Example – Step 12
1: r3[-1] = load(r1[0]) if p1[0]
2: r4[-1] = r3[-1] * 26 if p1[1]
4: r1[-1] = r1[0] + 4 if p1[0]
3: store (r2[0], r4[-1]) if p1[2]
5: r2[-1] = r2[0] + 4 if p1[2]
7: brlc Loop if p1[2]
Loop:
LC = 99
ESC = 2
p1[0] = 1
Finishing touches - Sort ops, initialize ESC, insert BRF and staging predicate,
initialize staging predicate outside loop
Unrolled
Schedule
1
2
3
4
5
7
Stage 1
Stage 2
Stage 3
Staging predicate, each
successive stage increment
the index of the staging predicate
by 1, stage 1 gets px[0]
0
1
2
3
4
5
6

## Slide 35: Example – Dynamic Execution of the Code
1: r3[-1] = load(r1[0]) if p1[0]
2: r4[-1] = r3[-1] * 26 if p1[1]
4: r1[-1] = r1[0] + 4 if p1[0]
3: store (r2[0], r4[-1]) if p1[2]
5: r2[-1] = r2[0] + 4 if p1[2]
7: brlc Loop if p1[2]
Loop:
LC = 99
ESC = 2
p1[0] = 1
0: 1, 4
1:
2: 1,2,4
3:
4: 1,2,4
5: 3,5,7
6: 1,2,4
7: 3,5,7
…
198: 1,2,4
199: 3,5,7
200: 2
201: 3,5,7
202: -
203 3,5,7
time: ops executed
Total time = II(num_iteration + num_stages – 1)
= 2(100 + 3 – 1) = 204 cycles