## Slide 1: EECS 583 – Class 13 Software Pipelining
University of Michigan
March 4, 2024

## Slide 2: Announcements + Reading Material
Project discussion meetings – Mar 11 (M 10am-12pm), Mar 13 (W 10am-12pm), Mar 14 (Th 10:30am-12pm)
  Each group meets 10 mins with Aditya, Yunjie, and I on Zoom, use GSI office hour link
    Don’t be late! Show up a couple of mins early to make sure you can connect, strict timing
    Come in with an idea or 2 to discuss about what you want to do, paper that you will base your work on
    Maximum of 2 ideas for the group (no time to discuss more)
  Google calendar signup available – see piazza post by Aditya – Please just sign up once!
Project proposals
  Due Monday, Mar 18, midnight
  1 paragraph summary of what you plan to work on
    Topic, what are you going to do, what is the goal, 1-2 references
  Email to me & Aditya & Yunjie, cc all your group members
Today’s class reading
  “Code Generation Schema for Modulo Scheduled Loops”, B. Rau, M. Schlansker, and P. Tirumalai, MICRO-25, Dec. 1992.
Next class
  “Register Allocation and Spilling Via Graph Coloring,” G. Chaitin, Proc. 1982 SIGPLAN Symposium on Compiler Construction, 1982.

## Slide 3: Recap: Software Pipelining Terminology
Iter 1
Iter 2
Iter 3
II
time
Initiation Interval (II) = fixed delay
between the start of successive iterations
Each iteration can be divided
into stages consisting of II cycles
each
Number of stages in 1 iteration
is termed the stage count (SC)
Takes SC-1 cycles to fill/drain the pipe

## Slide 4: Recap: Resource Usage Legality
Need to guarantee that
  No resource is used at 2 points in time that are separated by an interval which is a multiple of II
  I.E., within a single iteration, the same resource is never used more than 1x at the same time modulo II
  Known as modulo constraint, where the name modulo scheduling comes from
  Modulo reservation table solves this problem
    To schedule an op at time T needing resource R
      The entry for R at T mod II must be free
    Mark busy at T mod II if schedule
0
1
2
II = 3
alu1
alu2
mem
bus0
bus1
br

## Slide 5: Recap: Dependences in a Loop
Need worry about 2 kinds
  Intra-iteration
  Inter-iteration
Delay
  Minimum time interval between the start of operations
  Operation read/write times
Distance
  Number of iterations separating the 2 operations involved
  Distance of 0 means intra-iteration
Recurrence manifests itself as a circuit in the dependence graph
1
2
4
3
<1,1>
<1,0>
<1,2>
<1,2>
<1,0>
<delay, distance>
Edges annotated with tuple

## Slide 6: Dynamic Single Assignment (DSA) Form
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
Impossible to overlap iterations because each iteration writes to the same
register. So, we’ll have to remove the anti and output dependences.
Virtual rotating registers
* Each register is an infinite push down array (Expanded virtual reg or EVR)
* Write to top element, but can reference any element
* Remap operation slides everything down  r[n] changes to r[n+1]
A program is in DSA form if the same virtual register (EVR element) is never
assigned to more than 1x on any dynamic execution path
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
6: p1[-1] = cmpp (r1[-1] < r9)
remap r1, r2, r3, r4, p1
7: brct p1[-1] Loop
DSA
conversion

## Slide 7: Loop Dependence Example
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
6: p1[-1] = cmpp (r1[-1] < r9)
remap r1, r2, r3, r4, p1
7: brct p1[-1] Loop
1
2
3
4
5
6
7
In DSA form, there are no
inter-iteration anti or output
dependences!
Assume the compiler can prove the load and store are never dependent for this example!
1,0
1,0
0,0
3,0
2,0
1,1
1,1
1,1
1,1
0,0
<delay, distance>
r1 = &A
r2 = &B
Loop:

## Slide 8: Class Problem
1: r1[-1] = load(r2[0])
2: r3[-1] = r1[1] – r1[2]
3: store (r3[-1], r2[0])
4: r2[-1] = r2[0] + 4
5: p1[-1] = cmpp (r2[-1] < 100)
remap r1, r2, r3
6: brct p1[-1] Loop
Draw the dependence graph
showing both intra and inter
iteration dependences
Latencies: ld = 2, st = 1, add = 1, cmpp = 1, br = 1
1
2
3
4
5
6

## Slide 9: Class Problem Answer
1: r1[-1] = load(r2[0])
2: r3[-1] = r1[1] – r1[2]
3: store (r3[-1], r2[0])
4: r2[-1] = r2[0] + 4
5: p1[-1] = cmpp (r2[-1] < 100)
remap r1, r2, r3
6: brct p1[-1] Loop
Draw the dependence graph
showing both intra and inter
iteration dependences
Latencies: ld = 2, st = 1, add = 1, cmpp = 1, br = 1
1
2
3
4
5
6
1
2
3
4
5
6
<0,0>
<2,3>
<2,2>
<1,0>
<1,1>
<1,1>
<1,0>
<1,0>
<1,1>
<0,0>
Instructions 1-5 have <0,0>
control dependences to 6.
<1,0>
<1,1>
Red edges are memory anti and flow dependences

## Slide 10: Minimum Initiation Interval (MII)
Remember, II = number of cycles between the start of successive iterations
Modulo scheduling requires a candidate II be selected before scheduling is attempted
  Try candidate II, see if it works
  If not, increase by 1, try again repeating until successful
MII is a lower bound on the II
  MII = Max(ResMII, RecMII)
  ResMII = resource constrained MII
    Resource usage requirements of 1 iteration
  RecMII = recurrence constrained MII
    Latency of the circuits in the dependence graph

## Slide 11: ResMII
Simple resource model
A processor has a set of resources R. For each resource r in R
there is count(r) specifying the number of identical copies
Concept: If there were no dependences between the operations, what
is the the shortest possible schedule?
ResMII = MAX (uses(r) / count(r))
for all r in R
uses(r) = number of times the resource is used in 1 iteration
In reality its more complex than this because operations can have
multiple alternatives (different choices for resources it could be
assigned to), but we will ignore this for now

## Slide 12: ResMII Example
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
ALU: used by 2, 4, 5, 6
 4 ops / 2 units = 2
Mem: used by 1, 3
 2 ops / 1 unit = 2
Br: used by 7
 1 op / 1 unit = 1
ResMII = MAX(2,2,1) = 2
ResMII = MAX (uses(r) / count(r))
uses(r) = number of times the resource is used in 1 iteration

## Slide 13: RecMII
Approach: Enumerate all irredundant elementary circuits in the
dependence graph
RecMII = MAX (delay(c) / distance(c))
for all c in C
delay(c) = total latency in dependence cycle c (sum of delays)
distance(c) = total iteration distance of cycle c (sum of distances)
2
1
1,0
3,1
cycle
k 1
k+1 2
k+2
k+3
k+4 1
k+5 2
1
3
4 cycles,
RecMII = 4
delay(c) = 1 + 3 = 4
distance(c) = 0 + 1 = 1
RecMII = 4/1 = 4

## Slide 14: RecMII Example
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
1
2
3
4
5
6
7
1,0
1,0
0,0
3,0
2,0
1,1
1,1
1,1
1,1
0,0
<delay, distance>
4  4: 1 / 1 = 1
5  5: 1 / 1 = 1
4  1  4: 1 / 1 = 1
5  3  5: 1 / 1 = 1
RecMII = MAX(1,1,1,1) = 1
Then,
MII = MAX(ResMII, RecMII)
MII = MAX(2,1) = 2
RecMII = MAX(delay(c) / distance(c))
delay(c) = total latency in dependence cycle c (sum of delays)
distance(c) = total iteration distance of cycle c (sum of distances)

## Slide 15: Homework Problem
1: r1[-1] = load(r2[0])
2: r3[-1] = r1[1] – r1[2]
3: store (r3[-1], r2[0])
4: r2[-1] = r2[0] + 4
5: p1[-1] = cmpp (r2[-1] < 100)
remap r1, r2, r3
6: brct p1[-1] Loop
Calculate RecMII, ResMII, and MII
Latencies: ld = 2, st = 1, add = 1, cmpp = 1, br = 1
Resources: 1 ALU, 1 MEM, 1 BR
1
2
3
4
5
6
<0,0>
<2,3>
<2,2>
<1,0>
<1,1>
<1,1>
<1,0>
<1,0>
<1,1>
<0,0>

## Slide 16: Modulo Scheduling Process
Use list scheduling but we need a few twists
  II is predetermined – starts at MII, then is incremented
  Cyclic dependences complicate matters
    Estart/Priority/etc.
    Consumer scheduled before producer is considered
      There is a window where something can be scheduled!
  Guarantee the repeating pattern
2 constraints enforced on the schedule
  Each iteration begin exactly II cycles after the previous one
  Each time an operation is scheduled in 1 iteration, it is tentatively scheduled in subsequent iterations at intervals of II
    MRT used for this

## Slide 17: Priority Function
Height-based priority worked well for acyclic scheduling, makes sense
that it will work for loops as well
Acyclic:
Height(X) =
0, if X has no successors
MAX ((Height(Y) + Delay(X,Y)), otherwise
for all Y = succ(X)
Cyclic:
HeightR(X) =
0, if X has no successors
MAX ((HeightR(Y) + EffDelay(X,Y)), otherwise
for all Y = succ(X)
EffDelay(X,Y) = Delay(X,Y) – II*Distance(X,Y)

## Slide 18: Calculating Height
1
2
3
4
3,0
1,1
2,2
Insert pseudo edges from all nodes to branch with latency = 0, distance = 0 (dotted edges)
Compute II, For this example assume II = 2
HeightR(4) =
HeightR(3) =
HeightR(2) =
HeightR(1)
2,0
0,0
0,0
0,0

## Slide 19: Calculating Height Solution
1
2
3
4
3,0
1,1
2,2
Insert pseudo edges from all nodes to branch with latency = 0, distance = 0 (dotted edges)
Compute II, For this example assume II = 2
HeightR(4) = H(4) + (1 – II*1) (Assume H(4) is 0 since not calculated yet 0 + 1-2 = -1  0 (Always MAX answer with 0)
HeightR(3) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(2) + 2 – II*2 = 0 + 2 – 2*2 = -2) Assume H(2) is 0 since not calculated yet = 0
HeightR(2) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(3) + 2 – II*0 = 0 + 2 – 2*0 = 2) = 2
HeightR(1) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(2) + 3 – II*0 = 2 + 3 – 2*0 = 5) = 5
Now recalculate the heights to see if anything changes since HeightR(3) assumed wrong value for node 2 HeightR(3) = MAX(H(4) + 0 – II*0 = 0 + 0 – 2*0 = 0, H(2) + 2 – II*2 = 2 + 2 – 2*2 = 0) = 0  Unchanged, so no need to compute any other heights again
2,0
0,0
0,0
0,0

## Slide 20: The Scheduling Window
E(Y) =
0, if X is not scheduled
MAX (0, SchedTime(X) + EffDelay(X,Y)),
otherwise
With cyclic scheduling, not all the predecessors may be scheduled,
so a more flexible earliest schedule time is:
MAX
for all X = pred(Y)
Latest schedule time(Y) = L(Y) = E(Y) + II – 1
Every II cycles a new loop iteration will be initialized, thus every II
cycles the pattern will repeat. Thus, you only have to look in a
window of size II, if the operation cannot be scheduled there, then
it cannot be scheduled.
where EffDelay(X,Y) = Delay(X,Y) – II*Distance(X,Y)

## Slide 21: Loop Prolog/Epilog
Prolog
Epilog
Kernel
Disable using
predicated execution
Execute loop kernel on every iteration, but for prolog and epilog
selectively disable the appropriate operations to fill/drain the pipeline
Only the kernel involves executing full width of operations
Prolog and epilog execute a subset (ramp-up and ramp-down)

## Slide 22: Kernel-only Code Using Rotating Predicates
A0
A1 B0
A2 B1 C0
A B C D
Bn Cn-1 Dn-2
Cn Dn-1
Dn
P[0] P[1] P[2] P[3]
1 0 0 0
1 1 0 0
1 1 1 0
1 1 1 1
…
0 1 1 1
0 0 1 1
0 0 0 1
A if P[0] B if P[1] C if P[2] D if P[3]
A - - -
A B - -
A B C -
A B C D
…
- B C D
- - C D
- - - D
P referred to as the staging predicate

## Slide 23: Modulo Scheduling Architectural Support
Loop requiring N iterations
  Will take (N + (S – 1))*II cycles where S is the number of stages
2 special registers created
  LC: loop counter (holds N)
  ESC: epilog stage counter (holds S)
Software pipeline branch operations
  Initialize LC = N, ESC = S in loop preheader
  All rotating predicates are cleared
  SWP-BR (BRLC)
    While LC > 0, decrement LC and RRB, P[0] = 1, branch to top of loop
      This occurs for prolog and kernel
    If LC = 0, then while ESC > 0, decrement RRB and write a 0 into P[0], and branch to the top of the loop
      This occurs for the epilog

## Slide 24: Modulo Scheduling Example
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
6: p1 = cmpp (r1 < r9)
7: brct p1 Loop
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
for (j=0; j<100; j++)
b[j] = a[j] * 26
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
7: brlc Loop
Loop:
Loop:
LC = 99
Step1: Compute to loop into
form that uses LC

## Slide 25: Example – Step 2
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step 2: DSA convert
1: r3 = load(r1)
2: r4 = r3 * 26
3: store (r2, r4)
4: r1 = r1 + 4
5: r2 = r2 + 4
7: brlc Loop
Loop:
LC = 99

## Slide 26: Example – Step 3
1
2
3
4
5
7
1,1
3,0
2,0
1,1
1,1
1,1
1,1
RecMII = 1
RESMII = 2
MII = 2
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step3: Draw dependence graph
Calculate MII
0,0
0,0
No memory dependences since load and store refer to distinct arrays

## Slide 27: Example – Step 4
1: H = 5
2: H = 3
3: H = 0
4: H = 0
5: H = 0
7: H = 0
1
2
3
4
5
7
1,1
0,0
3,0
2,0
1,1
1,1
1,1
1,1
Step 4 – Calculate priorities (MAX height
to pseudo stop node)
0,0
0,0
0,0
0,0
0,0
0,0
1: H = 5
2: H = 3
3: H = 0
4: H = 4
5: H = 0
7: H = 0
Iter1
Iter2

## Slide 28: Example – Step 5
resources: 4 issue, 2 alu, 1 mem, 1 br
latencies: add=1, mpy=3, ld = 2, st = 1, br = 1
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Schedule brlc at time II - 1
alu0
alu1
mem
br
MRT
0
1
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
0
1
2
3
4
5
6

## Slide 29: Example – Step 6
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step6: Schedule the highest priority op
Op1: E = 0, L = 1
Place at time 0 (0 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
0
1
2
3
4
5
6

## Slide 30: Example – Step 7
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step7: Schedule the highest priority op
Op4: E = 0, L = 1
Place at time 0 (0 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
4
4
0
1
2
3
4
5
6

## Slide 31: Example – Step 8
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step8: Schedule the highest priority op
Op2: E = 2, L = 3
Place at time 2 (2 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
4
4
2
2
X
0
1
2
3
4
5
6

## Slide 32: Example – Step 9
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step9: Schedule the highest priority op
Op3: E = 5, L = 6
Place at time 5 (5 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
2
2
3
3
X
4
4
X
0
1
2
3
4
5
6

## Slide 33: Example – Step 10
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step10: Schedule the highest priority op
Op5: E = 5, L = 6
Place at time 5 (5 % 2)
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
2
2
3
3
X
4
4
X
5
X
5
0
1
2
3
4
5
6

## Slide 34: Example – Step 11
1: r3[-1] = load(r1[0])
2: r4[-1] = r3[-1] * 26
3: store (r2[0], r4[-1])
4: r1[-1] = r1[0] + 4
5: r2[-1] = r2[0] + 4
remap r1, r2, r3, r4
7: brlc Loop
Loop:
LC = 99
Step11: calculate ESC, SC = ceiling(max unrolled sched length / ii)
unrolled sched time of branch = rolled sched time of br + (ii*esc)
SC = 6 / 2 = 3, ESC = SC – 1
time of br = 1 + 2*2 = 5
alu0
alu1
mem
br
MRT
0
1
X
X
0
1
7
Rolled
Schedule
Unrolled
Schedule
1
1
X
2
2
3
3
X
4
4
X
5
X
5
7
0
1
2
3
4
5
6

## Slide 35: Example – Step 12
1: r3[-1] = load(r1[0]) if p1[0]
2: r4[-1] = r3[-1] * 26 if p1[1]
4: r1[-1] = r1[0] + 4 if p1[0]
3: store (r2[0], r4[-1]) if p1[2]
5: r2[-1] = r2[0] + 4 if p1[2]
7: brlc Loop if p1[2]
Loop:
LC = 99
ESC = 2
p1[0] = 1
Finishing touches - Sort ops, initialize ESC, insert BRF and staging predicate,
initialize staging predicate outside loop
Unrolled
Schedule
1
2
3
4
5
7
Stage 1
Stage 2
Stage 3
Staging predicate, each
successive stage increment
the index of the staging predicate
by 1, stage 1 gets px[0]
0
1
2
3
4
5
6

## Slide 36: Example – Dynamic Execution of the Code
1: r3[-1] = load(r1[0]) if p1[0]
2: r4[-1] = r3[-1] * 26 if p1[1]
4: r1[-1] = r1[0] + 4 if p1[0]
3: store (r2[0], r4[-1]) if p1[2]
5: r2[-1] = r2[0] + 4 if p1[2]
7: brlc Loop if p1[2]
Loop:
LC = 99
ESC = 2
p1[0] = 1
0: 1, 4
1:
2: 1,2,4
3:
4: 1,2,4
5: 3,5,7
6: 1,2,4
7: 3,5,7
…
198: 1,2,4
199: 3,5,7
200: 2
201: 3,5,7
202: -
203 3,5,7
time: ops executed
Total time = II(num_iteration + num_stages – 1)
= 2(100 + 3 – 1) = 204 cycles