## Slide 1: Ferroelectric Random Access Memory (FeRAM)
http://www.symetrixcorp.com/lib/images/Devices/SuperLatice_01.jpg
George Allen
Carl Stanfield
Guanye Zheng
EECS 373 Presentation
University of Michigan
11/27/2012

## Slide 2: History Dudley Allen Buck, graduate thesis, MIT 1952 "Ferroelectrics for Digital Information Storage and Switching" - http://hdl.handle.net/1721.3/40244

## Slide 3: Is FeRAM just a fancy version of DDR?
DDR
1T-1C cell
dielectric layer
read requires cap refresh
volatile
<50nm
refresh ~65ms
FeRAM
1T-1C cell
ferroelectric layer (PZT)
read requires cap refresh
non-volatile (sorta)
130nm
refresh not needed

## Slide 4: Read/Write process Read force cell to '0' state reorientation of atoms causes a pulse sent to driveline prior state was '1' - pulse is detected prior state was '0' - pulse not detected refresh state Write charge forces a polarity change
 | write '0' | write '1' | read
wordline | assert | assert | assert
bitline | gnd | vdd | float
driveline | vdd | gnd | vdd

## Slide 5: Why FRAM? Rough Comparison (1st generation)
source: TI's presentation on FRAM

## Slide 6: More Detailed / Overall Memory Products Comparison
source:http://www.fujitsu.com/emea/services/microelectronics/fram/technology/

## Slide 7: Memory Product Comparison On Power and Size
source: presentation (titled Novel Memory Architectures)
by Insoo Kim / Feng Wang, The Penn State Universitym on Mar. 23th, 2005

## Slide 8: FRAM vs EEPROM 1/30,000 Write Time 1/20 Energy -- 1/400 Power
source: http://www.fujitsu.com/emea/services/microelectronics/fram/technology/

## Slide 9: FRAM vs EEPROM 100,000 Times Better ENDURANCE
source: http://www.fujitsu.com/emea/services/microelectronics/fram/technology/

## Slide 10: FRAM vs FLASH Less Power and Faster Speed
source: http://www.ti.com.cn/mcu/cn/docs/mcuproductcontentnp.tsp?familyId=1751&sectionId=95&tabId=2840&family=mcu

## Slide 11: FRAM vs FLASH Much Better Endurance
source: http://www.ti.com.cn/mcu/cn/docs/mcuproductcontentnp.tsp?familyId=1751&sectionId=95&tabId=2840&family=mcu

## Slide 12: FRAM vs SRAM
SRAM is better at:
Price & Speed(not that much)
FRAM is more
Flexible
(all-in-one memories)
source: http://www.ti.com.cn/mcu/cn/docs/mcuproductcontentnp.tsp?familyId=1751&sectionId=95&tabId=2840&family=mcu

## Slide 13: FRAM vs DRAM
When density and price are most important
(for example, memories for pixels)
DRAM is best choice
FRAM cannot replace DRAM yet

## Slide 14: FRAM getting better at density!
Currently:
up to 4Mbits (according to TI's data)
Not as good as DRAM and SRAM
Better than EEPROM and FLASH
Expected:
As good as DRAM

## Slide 15: Take-away Point: FRAM combines Advantages!
source: http://www.ti.com.cn/mcu/cn/docs/mcuproductcontentnp.tsp?familyId=1751&sectionId=95&tabId=2840&family=mcu

## Slide 16: Application Benefits
Low Power Consumption
  Good For: Low energy access systems
  Reason: Write cycles require less power (RFID)
Fast Write Speed
  Good For: High noise environment
  Reason: Short write time limits window of vulnerability
High Endurance
  Good For: Diagnostic and maintenance systems
  Reason: No restriction of system state writes
Misc
  Resistant to Gamma Radiation (70kGray) unlike EEPROM
  AEC-Grade 1 adder cheaper than other nonvolatile memory

## Slide 17: Application Drawbacks
Low Storage Density
  Bad For: Storing large amounts of data
  Reason: Poor density compared to DRAM & SRAM
Higher Cost

## Slide 18: Current Applications
Automotive
  Shift-by-Wire/Navigation/Anti-Pinch Control
Computing
  Solid State Drive/LAN Bypass/Network Router
http://www.ramtron.com/applications/computing.aspx

## Slide 19: Current Applications
Metering
  Advanced Metering/Gaming/POS Systems
Industrial
  Motion Control/Process Controls
RFID/Wireless Memory
  Wireless Datalogging/Gamma Radiation
http://www.ramtron.com/applications/metering.aspx

## Slide 20: The Future of FRAM
Improved Storage Density
  Stacking
  3D integration
Improved Manufacturing Process
  Conventional process degrades ferroelectric layer
Reduction in Size
  Unknown charge density detection limit
  Theoretical performance unclear

## Slide 21: Q & A